## Slide 1: Exercise 1: OpCode Debugger

## Slide 2: Precondition
Download GIT
e.g https://git-scm.com/downloads
Create a folder where to install the course exercise
e.g. C:\Users\afin\code\
Open a shell where it’s possible to run GIT command and move to the created folder
e.g. In Window, using Git Bash in the created folder
Donwload the exercise code cloning the git repository
git clone https://github.com/antfin/ComputerProgrammingBasic.git
Download Python
e.g. https://www.python.org/downloads/
Donwload one code editor like Eclipse or PyCharm
e.g https://www.jetbrains.com/pycharm/download
https://www.eclipse.org/downloads/eclipse-packages/
Steps needed to run the exercise

## Slide 3: Virtual Microcontroller OpCodes
LD
LD_A
LD_N
ADD
DIV
ST
6 OpCodes are implemented into the microcontroller.py file

## Slide 4
LD(source_register, destination_register): Load the value of the source register into the destination register
CPU
00000000
Program Counter
11000100
Registers
R0
R1
R2
R3
Clock
00000000
11000100
00000000
EXAMPLE:
LD(2,0)  Load the value of Register 2 into Register 0

## Slide 5
Memory
LD_A(source_address, destination_register): Load the value of the source address into the destination register
CPU
00000000
Program Counter
00100111
Registers
R0
R1
R2
R3
Clock
00000000
11000100
00000000
EXAMPLE:
LD_A(12,0)  Load the value of Memory Address 12 into Register 0
...
01010110
00100111
00000010
Address 11
Address 12
Address 13
...
...
...

## Slide 6
LD_N(number, destination_register): Load the number value into the destination register
CPU
00000000
Program Counter
00000100
Registers
R0
R1
R2
R3
Clock
00000000
11000100
00000000
EXAMPLE:
LD_N(4,0)  Load the value 4 into Register 0

## Slide 7
ADD(first_register, second_register, destination_register): Add the value of the first and second registers and save the result into the destination register
CPU
00000000
Program Counter
11010101
Registers
R0
R1
R2
R3
Clock
00010001
11000100
00000000
EXAMPLE:
ADD(1,2,0)  Add the value of Register 1 and Register 2 and save the result into Register 0
+

## Slide 8
DIB(first_register, second_register, destination_register): Div the value of the first by the value of the second registers and save the result into the destination register
CPU
00000000
Program Counter
00010110
Registers
R0
R1
R2
R3
Clock
00101100
00000010
00000000
EXAMPLE:
DIV(1,2,0)  Div the value of Register 1 by Register 2 and save the result into Register 0
/

## Slide 9
Memory
ST(source_register, destination_address): Load the value of the source register into the destination memory address
CPU
00000000
Program Counter
00000010
Registers
R0
R1
R2
R3
Clock
00000000
11000100
00000000
EXAMPLE:
ST(0,13)  Load the value of Register 0 into Memory Address 12
...
01010110
00100111
00000010
Address 11
Address 12
Address 13
...
...
...

## Slide 10: Virtual Microcontroller Debugger
print_registers
print_data
print_overflow_flag
3 functions are use to debug what it’s happening inside the cpu